## Slide 1: Building Softwire in IPv6 Home Network
draft-liu-homenet-softwire-00

## Slide 2: Introduction
IPv6 Home Network needs to support IPv4 service
Discuss how to build softwire in homenet to provide IPv4 access
  Softwire: IPv4 over IPv6 tunneling mechanism, Hub and Spoke mode
    Including DS-Lite, MAP, lw4over6
Possible scenarios: Softwire initiated by
  A. All Home Routers
  B. Edge Router
  C. End Host

## Slide 3: A. Softwire Initiated by All Home Routers
ISP provide Softwire configuration to edge router in DHCPv6 options
  BR Address, IPv4 address, etc
Edge router advertises DHCPv6 options by HNCP
Routers build softwires accordingly
DO NOT need OSPF for IPv4
NO IPv4 traffic between home routers
Edge Router
ISP Network
Interior Routers
Hosts
HNCP
IPv4 over IPv6 Tunnel
IPv6 link
IPv6 link
Dual stack links

## Slide 4: Home Router Requirements
1. Support Softwire mechanisms
2. Enable Softwire when particular DHCPv6 options present in HNCP data:
  DS-Lite: OPTION_AFTR_NAME
  MAP-E: OPTION_S46_CONT_MAPE
  lw4over6: OPTION_S46_CONT_LW & OPTION_DHCP4_O_DHCP6_SERVER
  Disable Softwire when user explicitly disables IPv4

## Slide 5: Provisioning
Common
  IPv6 address of AFTR/BR: through HNCP (advertising DHCPv6 options)
DS-Lite
  No additional provisioning
MAP-E
  MAP rule: through HNCP (advertising DHCPv6 options)
Lightweight 4over6
  IPv4 address and port set: Each router runs DHCPv6 or DHCPv4 over DHCPv6 to get its own configuration

## Slide 6: Example: Running lw4over6
Edge Router
ISP Network
Interior Router
Host
DHCPv6 Prefix Delegation (OPTION_S46_CONT_LW & OPTION_DHCP4_O_DHCP6_SERVER)
HNCP advertisement (DHCPv6 options)
Each router gets an IPv4 address (and port set) (DHCPv4 over DHCPv6)
IPv6 ready
Build IPv4-in-IPv6 tunnel
IPv4 ready
Dual-stack Internet access

## Slide 7: B. Softwire Initiated by Edge Router
Edge Router (which connects to ISP) build IPv6 tunnel
  Perform NAT44 in MAP/lw4over6
Home network is a dual-stack network, use private IPv4 prefix, and run OSPF for IPv4
Edge Router
ISP Network
Interior Routers
Hosts
IPv4 over IPv6 Tunnel
IPv6 link
Dual Stack Homenet
OSPF for both IPv6/IPv4

## Slide 8: C. Softwire Initiated by End Host
Softwire information advertised to interior routers using HNCP, as in A.
Interior Routers provision DHCPv6 Softwire options to LAN hosts
Require softwire support in end host, difficult for large scale deployment
Edge Router
ISP Network
Interior Router
Hosts
IPv4 over IPv6 Tunnel
IPv6 link
IPv6 link
IPv6 link
Pure IPv6 Homenet

## Slide 9: Discussion
We recommend (A) to be used in Homenet
Draft status: -00 version completed
Any comments will be greatly helpful
Softwire Initiated by | Pros | Cons
A. All Home Routers | Homenet: pure IPv6 | Routers need to support Softwire mechanisms
B. Edge Router | No softwire-specific requirement for homenet | Homenet: dual stack Require OSPF for IPv4
C. End Host | Homenet: pure IPv6 | End hosts need to support softwire